GA.--- _

0041246062• 296062 RFOR D 1120525 DFCG X

TO: RF BREMEN

FROM: SONNE

14.12.87 / 06000TC SHORT REPORT

12.12. SONNE IN PRIMARY SEARCH AREA WITH EMPLOYED WITH MAPPING  XXXXX 07:30 ARRIVED AT SAR-OPS. TRANSFER TO SONNE BY TUG JOHN ROSS.

13.12. 09:00 XXXXX ARR. AT  SONNE

IN EARCH AREA (PRIM.S.A.) TWO  TUGS WOLRAAD WOLTEMADE AND JOHN ROSS EACH WITH 1 EASTPORT PINGER LOCATOR SYSTEM 20, AS WELL AS AS BACKUP A SOUTH AFRICAN STREAMERSYSTEM. SONNE FINISHES SEABEAM PROFILES. PROCESSING AND CORRECTIONS DURING THE DAY.

11:00 SONNE, START MAPPING SECONDARY SEARCH AREA. TRY TO MODIFY OWN SEARCH SYSTEM: DUKANE PINGER AS INTERROGATOR FOR ATNAV-TRANSPONDER, REPLY AS SIGNAL TO VESSEL. ON W.W. SOUTH AFRICAN SYSTEM IN USE, J.R. NOT OPERATIONAL.

23:00 SEABEAM-CHARTS (1:50.000) READY. SEARCH SYSTEM ON JOHN ROSS NOT OPERATIONAL.

19.12.

08:00 DELIVERY OF CHARTS PLANNED FOR 10:00.

TRIED TO ACTIVATE SEVERAL TIMES THE PLESSEY-SYSTEM, VIA OUR SA-REPRESENTATIVE ON BOARD.  THIS WAS STORED AS PER 12.12. IN JOHANNESBURG WITH KNOWLEDGE AND OBVIOUS APPROVAL OF SAA AND SAR-OPS.

PROFILES OF SEC.SEARCH A. WILL BE FINISHED BY 12:00 AND WILL SHIFT TO LOCATION OF  TEST-PINGER TO CHECK OWN EQUIPMENT AND TO COMPLETE PROCESSING OF CHARTS.

BE ON STANDBY FOR FURTHER INSTRUCTIONS FROM SAR-OPS UND SAA.

HERE, ALL RUNS WITH ROUTINE AND PRECISION.

REGARDS

PLUEGER / MUELLER / ABICH

246062 RFOR D 1120525 DFCG X

87-12-14 06.17

290SEC EOM, DEC 14 87, 06:21:28,